## Slide 1
Energetic particle environment as seen by SphinX
P. Podgorski1, O. V. Dudnik2, S. Gburek1, M. Kowalinski1, J. Sylwester1, M. Siarkowski1, S. Plocieniak1 , J. Bakala1
1Space Research Centre, Polish Academy of Sciences, 51-622 Wrocław, ul. Kopernika 11, Poland
2V.N. Karazin Kharkiv National University, Svobody Square 4, 61077, Kharkiv, Ukraine
Solar
photometer
in X-rays
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 2
SphinX mechanical construction outline
Safety Covers
EUV Filter
Calibrated Apertures
Moving Shutter
Fluorescence Filter
Detector Support
Copper Plate
Silicon PIN Detectors
Alignment Mirror
Linear Motor
Heat Sink
Preamplifiers
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 3
FET
Be Window
(thickness: 12.5 mm)
Si-PIN Detector
Area:
- D1: 25 mm2
- D2: 13 mm2
Thickness: 500 mm
Temperature Sensor
Thermoelectric Cooler
TO-8 Package
Mounting Stud
Chart: Amptek XR-100CR Si-PIN detector photoelectric efficiency
SphinX detector
Preamplifier:
Charge sensitive
Sensitivity: 1 mV/keV (typical)
Reset type
Negative output
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 4
Detector response to particles
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels
Preamp reset
High energy detector event
Shaped pulse
Continuous feedback capacitance charging by the detector leakage current (depends on detector temperature)

## Slide 5
SphinX operation modes
Basic mode:
provides only lightcurves in 4 energy bands,
active all time while SphinX operated.
Spectral mode:
provides spectra (256 channels),
active only for selected time periods.
Sequence mode:
provides full data – sequence of detector events recorded with their amplitudes and arrival times,
active most of the time,
allows for data reduction,
limited size of data buffer.
Counts
Energy bin
Noise
Low
High
Background
 | energy bins | 
Band | D1 | D2, D3
Noise | 0 - 24 | 0 - 16
Low | 25 - 50 | 17 - 50
High | 51 - 253 | 51 - 253
Background | 254 - 255 | 254 - 255
Photons above 15 keV
Particles
Preamp resets
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 6
Example of SphinX particle signal (Level 0, basic mode)
Detector lightcurves [c/s]
Latitude
Optical & X-ray shadow
Altitude
Particle signal (D1)
Particle signal (D2+D3+D4)
Particle signal (D1)
Detector D1 is sensitive to particles within SAA nad RB while D2 is sensitive mainly to particles within SAA.
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 7
Example of SphinX D1 particle signal (Level 0, sequence mode)
NRB
NRB
NRB
NRB
SRB
SRB
SRB
SRB
SAA
SAA
X-ray shadow
X-ray shadow
Particles and preamp resets
Particle events
Solar X-ray events
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 8
SphinX D1 particle signal
06.04.2009 – permanent D1 preamp malfunction
10.07.2009 – change of flight software:
Improvement of data quality in sequence mode
degradation of data quality in basic mode
22.09.2009 – change of flight software:
Allows for some corrections of data in basic mode
Condition of SphinX D1 particle signal:
20.02.2009 - 06.04.2009 – excellent D1 data quality (sequence mode allows for further improvements)
06.04.2009 - 10.07.2009 – deteriorated D1 data quality. The data may be useful for analysis after some corrections.
10.07.2009 - 22.09.2009 – insufficient D1 data quality for any analysis
22.09.2009 - 29.11.2009 – insufficient D1 data quality for any analysis (may be useful after some corrections).
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 9
Improvement of D1 particle signal quality
Uncorrected particle count rate
Particle count rate corrected for resets and dead time
Background level due to preamp resets (varies with detector temperature)
(Possible only for time period from 20.02.2009 to 06.04.2009)
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 10
SphinX D2 particle signal
Overall SphinX D2 particle signal:
SphinX D2 particle signal – background level:
SphinX D2 detector temperature:
Correction for background level:
[c/s]
[OC]
[c/s]
[c/s]
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 11
Reconstruction of Earth’s particle environment
Count rate distribution in geographic coordinates obtained from SphinX D2 detector (basic mode) after background level correction. The map is averaged over whole observation period from February 20 to November 29, 2009.
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 12
Longitude
Latitude
SAA
RB
D1/D2 count rate ratio
(normalized to respective detector areas)
Geographic coordinates of D1/D2 count rate ratio
SphinX sensitivity to particles
Number of events
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels
[O. V. Dudnik et al.
X-RAY SPECTROPHOTOMETER SPHINX AND PARTICLE SPECTROMETER STEP-F OF THE SATELLITE EXPERIMENT CORONAS-PHOTON – PRELIMINARY RESULTS OF JOINT DATA ANALYSIS,
Solar System Research, 2012, Vol. 46, No. 2, pp. 160–169]

## Slide 13
STEP-F
Satellite Telescope for measuring electrons and protons
V.N. Karazin Kharkiv National University, Ukraine
SphinX (incorporated within TESIS complex)
Solar photometer in X-rays
Space Research Centre, Polish Academy of Sciences
CORONAS-Photon satellite
SphinX – STEP-F joint data analysis
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 14
STEP-F is a telescope for measuring electron and proton fluxes aboard CORONAS-Photon satellite.
The STEP-F instrument provides registration of:
electron fluxes and energy spectra in the energy range Ee = 0.18 – 2.3 MeV,
electron fluxes in integral range Ee > 2.3 MeV,
proton fluxes and energy spectra in the energy range Ep = 3.5 - 55.2 MeV,
proton fluxes in integral range Ep > 55.2 MeV,
alpha-particle fluxes and energy spectra in the energy range Eа = 15.9 - 160.0 MeV.
SphinX – STEP-F joint data analysis
Registration channels used for common analysis:
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 15
An example of SAA particle flux in L-shell domain for four channels of STEP-F instrument and two SphinX channels.
dependence of L-shell positions at which maximum particle fluxes within SAA were observed on energy of electrons bound to the channels D2e and D1p of the STEP-F instrument.
Distribution of particle intensities by L-shells within SAA
Averaged energy thresholds for SphinX detectors in SAA:
Ethr1 ≈ 500keV (D1)
Ethr2 ≈ 475keV (D2)
(the values are not
strictly fixed)
[O. V. Dudnik et al.
X-RAY SPECTROPHOTOMETER SPHINX AND PARTICLE SPECTROMETER STEP-F OF THE SATELLITE EXPERIMENT CORONAS-PHOTON – PRELIMINARY RESULTS OF JOINT DATA ANALYSIS,
Solar System Research, 2012, Vol. 46, No. 2, pp. 160–169]
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 16
Changes of particle intensity distribution in nothern hemisphere due to geomagnetic storm as seen by SphinX
Initial values of L-shell positions of fluxes maxima in north hemisphere and DL displacement due to geomagnetic storm in dependency of electron energy
Distribution of particle intensities by L-shells within RB
Averaged energy thresholds for SphinX detectors in RB:
Ethr1 ≈ 5keV (D1)
Ethr2 ≈ 60keV (D2)
(the values are not
strictly fixed)
May 3, 2009 - quiet conditions before geomagnetic storm,
May 9, 2009 - initial recovery phase from the magnetic storm
[O. V. Dudnik et al.
X-RAY SPECTROPHOTOMETER SPHINX AND PARTICLE SPECTROMETER STEP-F OF THE SATELLITE EXPERIMENT CORONAS-PHOTON – PRELIMINARY RESULTS OF JOINT DATA ANALYSIS,
Solar System Research, 2012, Vol. 46, No. 2, pp. 160–169]
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 17
Comparison of SphinX and STEP-F daily particle maps
SphinX
SPEP-F
D1:
D2:
D1-p:
D1-e:
04.05.2009
ascending:
descending:
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 18
Comparison of SphinX and STEP-F daily particle maps
SphinX
SPEP-F
D1:
D2:
D1-p:
D1-e:
11.05.2009
ascending:
descending:
Science & Space Weather Opportunities for PROBA2, May 04, 2012, Royal Observatory of Belgium, Brussels

## Slide 19
Thank you